OpenParEM2D
Open Parallel Electromagnetic 2D - A free, open-source electromagnetic simulator for 2D waveguides and transmission lines.
Features
- Full-wave solver
  - simultaneously solves the electric and magnetic fields
- Advanced finite-element method (FEM) with arbitrary high-order elements
- Adaptive mesh refinement
- Parallel processing through the Message Passing Interface (MPI)
- Front-end input file builder for common transmission line and waveguide types.
- Licensed under GPLv3 or later.
Capabilities
- Calculations
  - propagation constant
  - characteristic impedance
  - dielectric loss
  - conductor loss
  - surface roughness loss
  - field distributions
- Dominant and higher-order modes
- Arbitrary cross sections
- Arbitrary high frequencies
v.1.1

---
Workflow without “builder”
OpenParEM2D is a command-line tool with text inputs and outputs
Use with open source tools to create a complete workflow
Workflow used for development:
text editor
Arbitrary Cross Section
FreeCAD
export modes and boundary conditions file
project setup file
export drawing file
export mesh file
gmsh
text editor
material database file
library and/or local
ParaView input files
CSV file
OpenOffice
ParaView

---
Workflow with “builder”
For transmission line and waveguide types supported by the front-end tool “builder”, the flow is greatly simplified.
builder
project setup file
export modes and boundary conditions file
text editor
export drawing file
export mesh file
gmsh
text editor
material database file
library and/or local
ParaView input files
CSV file
Supported as of This Writing
rectangular waveguide
microstrip
symmetric coupled microstrip
asymmetric coupled microstrip
stripline
symmetric coupled stripline
asymmetric coupled stripline
OpenOffice
ParaView

---
Sample Results
E
H
2nd-order
elements
2nd-order
1/8 Coax
using symmetry
Coax
E real
Cutoff
TE11 Mode
4th-order
WR90
Rectangular Waveguide
H imag
PMC
PMC
PMC

---
E
E
E
H
H
3rd-order
H
E
E
H
H
3rd-order
Stripline
with etch profile
Coupled Microstrip
er=1
E
H
er=2.45
6th-order elements
Mesh Shown
No Adaptive Refinement
Partially-Filled Rectangular Waveguide
Even Mode
Odd Mode

---
Mesh at iteration 1
E tangential at iteration 20
Mesh at iteration 20
H tangential at iteration 20
Odd Mode of Coupled Microstrip
PEC
PEC