OpenParEM2D
Specifications
v.1.3

---
Specifications
OpenParEM2D is a command line tool that uses text files for all inputs. There are four required input files, and each has a specification.
All numbers are entered as MKS units without qualifiers. For example, 1 GHz is entered as 1e9.
The four input files with specifications are:
- project
- boundary conditions and modes
- materials
- mesh

---
Project File Specification
- The project file is a text file that uses keyword/value pairs to control the simulation.
- Use one keyword/value pair per line.
- Each keyword has a default value, so every keyword/value pair is optional.
- Keywords can appear in the file more than once, and excepting frequency.plan.* and field.point, the last entry is the one that is used.
  - Note: No error message or warning is issued when keyword values are overwritten.
- The first line of the file must be
#OpenParEM2Dproject 1.0

---
Project File Keyword/Value Pairs
#OpenParEM2Dproject 1.0 // required on first line
project.save.fields bool // Saves the files needed for ParaView to plot the fields.
mesh.file string // File name for the mesh file.
mesh.order int // Order of the finite elements used in the mesh.
        // 1 → linear, 2 → quadratic, etc.
mesh.refinement.cutoff double // mesh elements less than mesh.refinement.cutoff x max mesh error
        // are not refined.
mesh.refinement.fraction double // The fraction of the mesh to refine at each iteration
mesh.uniform_refinement.count int // The mesh is uniformly subdivided across all mesh elements
        // by the provided number.
mesh.enable.refine bool // Used when running OpenParEM2D from OpenParEM3D. Generally, the user
        // should not use this setting. default=1.
mode.definition.file string // File name for the boundary condition/mode file. Applies to both modal and
        // line style of impedance calculation. See the specification for this file.
materials.global.path string // Path to a global materials file serving as a library.
        // May also leave blank or use ./ for the local directory.
materials.global.name string // File name for the global materials file.
        // See the specification for this file.
materials.local.path string // Path to a local materials file serving as a library.
        // May also leave blank or use ./ for the local directory.
materials.local.name string // File name for the local materials file.
        // See the specification for this file.
materials.check.limits bool // Check the material values against range limits.
        // Set to false if the range limits are not appropriate.
refinement.frequency string // Sets frequency or frequencies on which adaptive mesh refinement is applied.
        // Options:
        // none - refine at no frequencies and simulate with the initial mesh
        // all - refine at each frequency starting from the initial mesh
        // high - refine at the highest frequency then simulate at all
        // frequencies with that mesh
        // low - refine at the lowest frequency then simulate at all
        // frequencies with that mesh
        // highlow - refine at the highest then lowest frequencies then simulate
        // at all frequencies with that mesh
        // lowhigh - refine at the lowest then highest frequencies then simulate
        // at all frequencies with that mesh
        // plan - refine at the frequencies marked in the frequency plan then
        // simulate at all frequencies with that mesh

---
refinement.variable string // Sets the variable used to determine refinement convergence
        // Options: alpha, beta, |gamma|, |Zo|, Re(Zo), Im(Zo)
        // A comma-separated list can be provided with the refinement variable
        // set per mode in order, with the final entry setting the refinement
        // variable for following modes. Examples:
        // refinement.variable |Zo| - refine all modes on |Zo|
        // refinement.variable |Zo|,|gamma| - refine mode 1 on |Zo| and
        // all other modes on |gamma|
        // refinement.variable beta,alpha,|Zo| - refine mode 1 on beta, mode 2
        // on alpha, and all others on |Zo|
refinement.iteration.min int // Minimum number of iterations to perform.
refinement.iteration.max int // Maximum number of iterations to perform.
refinement.required.passes int // The number of consecutive iterations that must meet the refinement
        // tolerance.
refinement.tolerance double // Tolerance for convergence during adaptive refinement.
frequency.plan.log string // Adds solution frequencies to the frequency plan using a log scale with
        // the comma-separated list start,stop,pointsPerDecade.
frequency.plan.log.refine string // Same as above plus mesh refinement is applied at these frequencies.
frequency.plan.linear string // Adds solution frequencies to the frequency plan using a linear scale with
        // the comma-separated list start,stop,step.
frequency.plan.linear.refine string // Same as above plus mesh refinement is applied at these frequencies.
frequency.plan.point double // Adds the given solution frequency to the frequency plan.
frequency.plan.point.refine double // Same as above plus mesh refinement is applied at the given frequency.
// Any number of frequency.plan.* lines can be specified.
// Overlapping frequencies are ok because duplicates are omitted.
// Mesh refinement is done in the order that the refinement frequencies are specified.
solution.modes int // number of modes to solve
solution.temperature double // Solution temperature, which is used for materials selection.
solution.tolerance double // Tolerance for the eigenvalue solution and H field calculation.
        // Can be set as a comma-separated list to provide values per mode.
        // See refinement.variable on how the values are applied to the modes.
solution.iteration.limit int // Iteration limit for the iterative eigenvalue and Hfield solvers.
solution.modes.buffer int // Additional number of modes over solution.modes to solve.
        // Increase this value if not all of the solution.modes solutions are found.

---
solution.impedance.definition string // Sets the definition to use for the characteristic impedance calculation.
        // Options: VI, PV, PI, or none, where none omits the calculation.
solution.impedance.calculation string // Sets the style of the setup for the characteristic impedance calculation.
        // Options: modal,line
solution.check.closed.loop bool // Check if current loops are closed.
solution.accurate.residual bool // Sets an input parameter to the eigenvalue solver that may produce higher
        // accuracy results. In many cases, the eigenvalue solver will hang with
        // this is set to true.
solution.shift.invert bool // Sets the eigenvalue solver to use the shift-and-invert method.
solution.use.initial.guess bool // Use the current solution as the initial guess in the next iteration.
solution.initial.alpha double // Initial value for alpha. Used with OpenParEM3D.
solution.initial.beta double // Initial value for beta. Used with OpenParEM3D.
solution.shift.factor double // A multiplier of the initial guess eigenvalue.
output.show.refining.mesh bool // Show details about the mesh during adaptive refinement.
output.show.postprocessing bool // Show details about the post-processing steps after the eigenvalue solution
        // is found.
output.show.iterations bool // Show the iterations during the eigenvalue solution.
output.show.license bool // Show the license governing use of the software.
test.create.cases bool // Create test cases useful for setting up regression testing.
test.show.audit bool // Show audit results when regression testing with the program called
        // “process”. This keyword is not used by OpenParEM2D.
test.show.detailed.cases bool // Show detailed information about the test cases when regression testing with
        // the program called “process”. This keyword is not used by OpenParEM2D.
debug.show.memory bool // Show memory usage at strategic times to look for memory leaks.
debug.show.project bool // Show the full set of project keywords and their values.
debug.show.frequency.plan bool // Show the full set of simulation and refinement frequencies.
debug.show.materials bool // Show the full set of materials from the material databases.
debug.show.mode.definitions bool // Show the setups used for mode definitions.
debug.show.impedance.details bool // Show all voltages, currents, powers, and impedance calculations. debug.skip.solve bool // Perform all operations but skip the solve.
debug.tempfiles.keep bool // Keeps the temporary files.
field.point double,double // x,y coordinate at which to calculate the E and H field values.
        // Any number of field.point keyword/value pairs can be specified.

---
Boundary/Mode File Specification
// This file specifies the physical locations of boundaries and modes along with information regarding type.
// Path definitions define physical placement, then boundaries and modes use the paths to complete the setup.
// Paths can be reused across boundaries and modes for simpler setup.
// a comment
#OpenParEMmodes 1.0 // required on first real line
// All coordinates are in m.
// This block is informational use only.
// Only one File/EndFile block can be specified.
File
   name=string // name of the file from which the lines are generated
EndFile
// Paths are used to define voltage integration lines, current integration loops,
// and locations for boundary conditions.
// Any number of paths can be defined.
// Paths are not required to be used.
// Names must be unique within all path definitions.
Path
   name=string
   point=(double,double) // (x,y)
   point=(double,double) // any number of points
   ...
   point=(double,double)
   closed=bool // false if the path is open and true if the path is closed
EndPath
// For closed loops, do not duplicate the starting and stopping points. Using closed=true
// closes the loop during calculations.

---
// Specify any number of boundaries.
// The physical placement of the boundary is defined by the paths.
// One path can be used if it is complete, and paths can be chained together to form more complex physical setups.
// Names must be unique within all boundary definitions.
Boundary
   name=string
   type=surface_impedance|perfect_electric_conductor|perfect_magnetic_conductor
   material=string // required for surface impedance
   path=name1 // no sign means that the direction of the path is unchanged
   path-=name2 // minus sign means that the direction of the path is reversed
   ...
   path+=name3 // plus sign means that the direction of the path is unchanged
EndBoundary
// Specify any number of modes.
// Use with solution.impedance.calculation set to “modal”.
// One Mode/EndMode block is applied to one solved waveguide/transmission line mode. N modes requires N blocks.
// For N modes, all mode numbers are required from 1 to N, so mode definitions are required for modes 1, 2, ..., N.
// One path can be used if it is complete, and paths can be chained together to form more complex physical setups.
// One voltage definition and/or one current definition can be provided per mode number.
// 0 is not an allowed mode number
Mode
   mode=integer
   type=voltage|current
   path=+name
   path-=name
   ...
   path=name
EndMode
// Specify any number of lines.
// Use with solution.impedance.calculate set to “line”.
// One Line/EndLine block is applied to each conductor. N conductors requires N blocks.
// For N lines, all line numbers are required from 1 to N, so line definitions are required for lines 1, 2, ..., N.
// One path can be used if it is complete, and paths can be chained together to form more complex physical setups.
// One voltage definition and/or one current definition can be provided per line number.
// 0 is not an allowed line number
Line
   line=integer
   type=voltage|current
   path=+name
   path-=name
   ...
   path=name
EndLine

---
// The Mode/EndMode and Line/EndLine blocks are interchangeable. Two block types are supported
// so that the block naming is coordinated with the impedance calculation type.

---
Materials File Specification
// This file specifies how materials are defined for use in OpenParEM2D. Dielectrics can be specified with a
// Debye model or by properties at a single frequency or a list of frequencies. Conductors are specified by properties
// at a single frequency or a list of frequencies.
// OpenParEM2D allows two material files to be specified: global and local. The global file can be a general
// materials library, and the local file can represent a specialized set of materials for the project. When both
// global and local material files are specified, the local materials file takes precedence over the global file
// when the same material name is used in both.
// a comment
#OpenParEMmaterials 1.0 // required on first real line
// All units are MKS
// meter, Ohms, Hz, S/m, Celcius
// Any number of Material blocks can be specified.
// Debye model
// dielectric only
Material
   name=text
   Temperature
      {temperature||temp||t}={double||any} // “any” means that the model applies at all temperatures
      {epsr_infinity||er_infinity}=double
      {delta_epsr||delta_er}=double
      m1=double
      m2=double
      {relative_permeability||mur}=double
      {loss_tangent||tand||tandel||conductivity||sigma)=double
   EndTemperature
   ... more Temperature blocks, optional
   Source
      any text
      any text
      ...
      any text
   EndSource
   ... more Source blocks, optional
EndMaterial

---
// frequency list
// dielectrics or metals
// linear interpolation supported
// extrapolation not supported
Material
   name=text
   Temperature
      {temperature||temp||t}={double||any} // “any” means that the model applies at all temperatures
      Frequency
        {frequency||freq||f}={double||any} // “any” means that the model applies at all frequencies
        {relative_permittivity||er||epsr}=double
        {relative_permeability||mur}=double
        {loss_tangent||tand|||tandel||conductivity||sigma)=double
        Rz=double // for surface roughness if a conductor
      EndFrequency
      ... more Frequency blocks, optional
   EndTemperature
   ... more Temperature blocks, optional
   Source
      any text
      any text
      ...
      any text
   EndSource
   ... more Source blocks, optional
EndMaterial

---
Mesh File Specification
- OpenParEM2D supports the gmsh mesh file version 2.2.
- See https://gmsh.info/
- The gmsh manual includes specifications of all versions of gmsh mesh formats including legacy versions like 2.2.