builder
Specifications
v.1.0

---
builder
- builder is a command line tool that uses a single text file for all inputs.
- It produces three output text files for use in quickly building projects for solution with OpenParEM2D
  - *.geo - geometrical input file for gmsh
  - *_modes.txt - boundary/modes file for OpenParEM2D
  - *.proj - Control project file for OpenParEM2D
- Supported transmission lines and waveguides
  - rectangular waveguide
  - microstrip
  - symmetric coupled microstrip
  - asymmetric coupled microstrip
  - stripline
  - symmetric coupled stripline
  - asymmetric coupled stripline

---
Rectangular Waveguide
conductor_material_top
material
conductor_material_bottom
width
height
conductor_material_right
conductor_material_left

---
Strip
upper_groundplane_material
upper_material
trace_material_sides
trace_etch_angle
(90 is square)
trace_thickness
upper_thickness
soldermask_thickness
trace_material_top
optional soldermask
trace_material_bottom
soldermask_material
trace_width
left_side_gap
right_side_gap
lower_thickness
lower_material
lower_groundplane_material
Use for microstrip and stripline.
left_side_material
right_side_material

---
CoupledStrip
upper_thickness
upper_groundplane_material
upper_material
trace_etch_angle
(90 is square)
trace_thickness
soldermask_thickness
trace_material_sides
trace_material_top
optional soldermask
trace_material_bottom
soldermask_material
trace_air_gap
trace_left_width
trace_right_width
left_side_gap
right_side_gap
lower_material
lower_groundplane_material
lower_thickness
Use for symmetric and asymmetric coupled microstrip and stripline.
left_side_material
right_side_material

---
builder File Specification
- The builder input file is a text file that uses keyword/value pairs to control the build.
- Use one keyword/value pair per line.
- Keywords can appear in the file more than once, and the last entry is the one that is used.
  - Note: No error message or warning is issued when keyword values are overwritten.
- The first line of the file must be
#builder 1.0

---
builder File Keyword/Value Pairs
#builder 1.0
// enable multiple definitions in one file
// call out the one to build here
Control
   build=name
   check_limits={true|false}
EndControl
// The "include=name" option pulls in data from the named case to enable a change from one case to propagate to others.
// When used, any further data included in the block supersedes the included data.
// The included data must be in the same file.
RectangularWaveguide
   name=string
   [include=name]
   width=double
   height=double
   material=string
   // set conductor material to "PEC" (without the quotes) for no conductor losses
   default_conductor_material=string // this is optional if all 4 of the materials below are specified
   // material overrides useful for varying surface roughness; can also specify PEC or PMC
   [conductor_material_top=string]
   [conductor_material_bottom=string]
   [conductor_material_left=string]
   [conductor_material_right=string]
EndRectangularWaveguide

---
// Use Strip to define microstrip and stripline.
Strip
   name=string
   [include=name]
   use_symmetry={true|false} // faster solve time when true
        // user must divide the impedance result by 2
   default_conductor_material=string // optional if all other materials are specified
   left_side_gap=double // measured from the farthest leftward extension of the trace
   [left_side_material=string] // a material, PEC, or PMC
   right_side_gap=double // measured from the farthest rightward extension of the trace
   [right_side_material=string] // a material, PEC, or PMC
   upper_thickness=double // measured from the top of the lower thickness
   upper_material=string
   [soldermask_thickness=double] // thin soldermasks can cause numerical problems in the solution
   [soldermask_material=string] // required for a non-zero soldermask thickness
   lower_thickness=double
   lower_material=string
   trace_thickness=double
   trace_width=double // width applies at the bottem next to the substrate
   trace_etch_angle=double // degrees; 90 for vertical
   // material overrides useful for varying surface roughness or applying symmetry
   [trace_material_bottom=string]
   [trace_material_top=string]
   [trace_material_sides=string]
   [upper_groundplane_material=string] // planes and sides can also specify PEC or PMC to create
        // symmetric coupled lines
   [lower_groundplane_material=string]
EndStrip

---
// Use CoupledStrip to define symmetric and asymmetric microstrip and stripline pairs.
CoupledStrip
   name=string
   [include=name]
   default_conductor_material=string // optional if all other materials are specified
   left_side_gap=double // measured from the farthest leftward extension of the trace
   [left_side_material=string] // a material, PEC, or PMC
   right_side_gap=double // measured from the farthest rightward extension of the trace
   [right_side_material=string] // a material, PEC, or PMC
   upper_thickness=double // measured from the top of the lower thickness
   upper_material=string
   [soldermask_thickness=double] // thin soldermasks can cause numerical problems in the solution
   [soldermask_material=string] // required for a non-zero soldermask thickness
   lower_thickness=double
   lower_material=string
   trace_left_width=double // width applies at the bottem next to the substrate
   trace_right_width=double // width applies at the bottem next to the substrate
        // set to 0 to force trace_right_width=trace_left_width for symmetric pair
   trace_thickness=double
   trace_air_gap=double // measured from from edge-to-edge at the bottom next to the substrate
   trace_etch_angle=double // degrees; 90 for vertical
   // material overrides useful for varying surface roughness or applying symmetry
   [trace_material_bottom=string]
   [trace_material_top=string]
   [trace_material_sides=string]
   [upper_groundplane_material=string] // planes and sides can also specify PEC or PMC to create
        // symmetric coupled lines
   [lower_groundplane_material=string]
EndCoupledStrip